|  | ......................... pcs. .............................. € .............................. € GEZE Slimline fanlight opener OL 90 N Activation via spring hinge reverser with hand lever For daily aeration and ventilation with vertically installed rectangular windows with bottom-hung, top-hung or side-hung casements, inward opening. Installation can be carried out from the front, without visible attachment screws. Casement is fitted with safety catch and locking device in the scissors. Casement closing pressure must be adjusted at the casement bracket. For window cleaning, the scissors can be disengaged quickly by pressing the release catch. Rod must be covered using an aluminium profile. Clearance-free activation via spring hinge reverser and with hand lever. Technical data: Opening width: 170 mm Leaf width: ........ mm ( ) 1 scissors for casement widths from 380 - 1200 mm1) ( ) 2 scissors for casement widths from 1200 - 2400 mm1) ( ) 3 scissors for casement widths from 2400 - 3600 mm1) 1) Heed panel weights Casement height: ........ mm (min. 250 mm) Centre of rod to lower edge Hand lever base plate: ........ mm Colour: ( ) silver-coloured EV1 ( ) dark bronze ( ) white, 9016 ( ) RAL shade according to choice Note: When used on bottom-hung casements, we prescribe the use of separate safety scissors for product liability reasons. These represent an additional safety feature which guarantees the permanent connection of casement and frame, e.g. GEZE FPS. |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE FPS gripping and cleaning scissors ( ) Size 1 from casement height 360 mm ( ) Size 2 from casement height 540 mm ( ) Size 3 from casement height 740 mm |