|  | ......................... pcs. .............................. € .............................. € GEZE E 170 scissor drive For daily aeration and ventilation and the safe and fast smoke dissipation at vertically installed, inwards opening bottom-hung, top-hung, side-hung, pivot leaf or turn leaf windows. Scissor drive with aluminium housing in a low-profile design with clear linear guide in 230 V version. Max. space requirements of 38 mm on window frames and leaves must be guaranteed. Installation must be from the front using invisible attachment screws. Leaf is fitted with safety catch and locking device in the scissors. Leaf closing pressure must be adjusted at the leaf bracket. Stroke 170 mm with variable stroke adjustment for simple regulation of opening width. End position cut-off in retracted and extended position must be triggered by limit switches. Delivered as a completely pre-mounted unit. Technical data: Current consumption: 230 V max. 0.4 A Enclosure rating: IP52 Ambient temperature: -5 °C to +60 °C Version: ( ) 230 V Type of window: ( ) bottom-hung leaf ( ) top-hung leaf ( ) side-hung leaf ( ) pivot leaf ( ) turn leaf ( ) inwards Leaf dimensions: ........ mm width (min. 550 mm – max. 1200 mm ) ........ mm height (min. 300 mm -> depending on the type of window and panel weight or leaf weight) Leaf material: ( ) Wood ( ) Aluminium ( ) Plastic Opening width: ..... mm or max. 170 mm (to be completed by the bidder) Colour: ( ) EV1 ( ) white, 9016 ( ) Shade according to choice ......... Note: When used on bottom-hung leaves, we prescribe the use of separate safety scissors for product liability reasons, e.g. GEZE FPS. |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Optional: ( ) Locking module for GEZE E 170 and E 170/2 scissor drives: Modular set for additional locking combined with the GEZE scissor drive ( ) Set variable cover: Individual extension of the standard drives |
|  | ......................... pcs. .............................. € .............................. € GEZE FPS gripping and cleaning scissors ( ) Size 1 from leaf height 360 mm ( ) Size 2 from leaf height 540 mm ( ) Size 3 from leaf height 740 mm |
|  | ......................... pcs. .............................. € .............................. € Installation and functional test Installation and functional test by an expert authorised by the manufacturer. |
|  | ......................... pcs. .............................. € .............................. € Start-up and official approval Official approval of the complete smoke and heat extraction system by an officially recognised expert, who also hands over the acceptance certificates. |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing of hold-open systems (optional position) Service package for maintenance and testing according to ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance and accident prevention inspection in accordance with ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to € 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Delivery and installation Wiring to be carried out on site by an electrical contractor according to the GEZE cable plan. Delivery, installation and commissioning through plant fitters or service partner. Safety analysis, instruction of the operator as to how the system works and handing over of the documentation. Annual maintenance and technical inspection by an expert authorised by the manufacturer incl. documentation of the inspection in an inspection log. |