|  | ......................... pcs. .............................. € .............................. € Integrated door closer system GEZE Boxer ISM, for double-leaf doors, closing force size 3 – 6 in accordance with EN 1154; for single-action doors from 50 mm door leaf thickness, guide rail with integrated mechanical closing sequence control in accordance with EN 1158. Vandalism protection against wilful maloperation of the closing sequence control, closing force, closing speed, hydraulic back check and latching action are adjustable after installation. Area of application Door width: min.: 1300 mm max.: 2800 mm Colour: ( ) silver-coloured Accessories: ( ) Integrated almost invisible flexible opening restrictor for E/R/ISM guide rails |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE carry bar CB flex with GEZE door closer design, for guaranteeing the correct closing sequence for all 2-leaf GEZE door closer systems with door closing sequence control, length in installed state is infinitely variable adjustable (70 - 210 mm overhang), non-visible hinge and length adjustment mechanisms, with cover cap at the side, can be cut to size on site, painted surface as standard. Colour: ( ) silver-coloured ( ) acc. to RAL |
|  | ......................... pcs. .............................. € .............................. € GEZE hold-open magnets, Operating voltage 24 V DC, Power consumption 1.5 W Retention force 490 N ( ) Hold-open magnet basic model (zinc plated without base plate) for in-wall installation or installation in any construction ( ) Hold-open magnet for wall mounting with base plate ( ) Hold-open magnet for flush-mounted installation ( ) Hold-open magnet for surface installation ( ) Base for hold-open magnet surface-mounted for floor installation ( ) Hold-open magnet with spacer tube zinc plated for floor/ceiling/wall mounting with swivelling magnetic head ( ) Version in basic length 185 mm ( ) Version in basic length 335 mm ( ) Hold-open magnet wall mounting, basic length 65 mm GEZE Magnetic counter plates, ( ) Standard magnetic counter plate on mounting plate with spring system for flatness with hold-open magnet ( ) Magnetic counter plate with spring buffer on installation housing with damping spring for soft spring buffer for heavy doors ( ) Magnetic counter plate, swivelling on mounting plate with swivelling magnetic counter plate for angle positions between door and hold-open magnet |
|  | ......................... pcs. .............................. € .............................. € GEZE current interruption switch (compulsory for hold-open magnets and freeswing function) ( ) Surface-mounted ( ) Flush-mounted |