|  | ......................... pc. € .............................. € .............................. Panic motor lock set GEZE IQ lock EL DL for double-leaf doors Self-locking panic motor lock GEZE IQ lock EL DL with mechanical strike box and all required and tested components for double-leaf full panic doors in accordance with EN 179 and EN 1125! The moving leaf is also unlocked upon panic release of the fixed leaf. Panic unlocking via latch or panic bar Self-unlocking of both door leaves Changeover function for unlocking from the outside and integrated electrical escape and child proofing to counteract misuse Divided and separated cross latch for absolute unencumbered crossbar projection without jamming even when preloaded! Operating modes: night-time operation, secured by day and permanently open Secured by day operation: door opener function by means of targeted locking or release of the cross latch Night-time operation: steel bolt 20mm throw bolt lock / motorised bolt entry less than 1 sec. Permanently open: bolt withdrawn and cross latch is not locked All required contacts are integrated in the lock and provide potential-free feedback: Deadbolt contact (with 95 % crossbar projection) Latch contact (with latch activation 10°) Cylinder contact Auxiliary lock contact (door open/door leaf enclosed) Release contact (bolt completely in lock case and cross latch loose) In case of fire alarm or power cut automatic changeover to mechanical basic and panic function as well as self-locking. Prepared for installation of profile lock cylinders and with 9 mm square nut. Closed and corrosion-resistant steel lock case in DIN sizes, front metal and strike box of stainless steel, lock can be used for DIN left and right doors without conversion Nominal voltage: 12-24 V DC Current consumption: temporarily 250 mA at 24V; 500 mA at 12V (incl. control unit) Supplied in a set comprising: 1 pc motor mortise lock IQ lock EL DL 1 pc mechanical strike box IQ lock DL with front metal 1 pc motor lock control MST 210 1 pc connecting cable 12-core, 10 m 1 pc cable duct open 1 pc reed switch contact set 1 pc strike plate for receiving the lock upwards 1 pc switch lock 1 pc tubular pipe for locking upwards 1 pc solid rod for locking downwards 1 pc rod guide 1 pc floor lock hollow ( ) IQ lock EL DL 9235 (distance 92 mm, backset 35 mm) ( ) IQ lock EL DL 9240 (distance 92 mm, backset 40 mm) ( ) IQ lock EL DL 9245 (distance 92 mm, backset 45 mm) ( ) IQ lock EL DL 7255 (distance 72 mm, backset 55 mm) ( ) IQ lock EL DL 7265 (distance 72 mm, backset 65 mm) ( ) IQ lock EL DL 7280 special backset 80 mm ( ) IQ lock EL DL 7210 special backset 100 mm Accessories: ( ) 1 pc. power supply 24 V DC part no. 109637 For use in escape and rescue routes or in fire protection doors, fittings are required in accordance with EN 179 or EN 1125:. For approved fittings, please refer to the currently valid certificate versions 0757-CPR-229-7013137-5-2 / 0757-CPR-229PANIK-7013137-4 to certify the durability. Only GEZE components tested and approved together in accordance with EN 179 and EN 1125 may be installed! To ensure all functions of the IQ lock EL DL a door closer system with closing sequence control and a carry bar are to be fitted. A suitable swing door drive can also be used on the moving leaf due to the motorised unlocking of the IQ lock EL DL. GEZE recommends ( ) 2 pc TS 5000 part no. 027333 ( ) 1 pc ISM guide rail part no. 115549 plus ( ) 2 pc GEZE panic bars (EN 1125) configurable part no. 119005 |
| --- | --- |